1. EnviroCorp is a dynamic, rapidly growing co-generation power company.  It is considering multiple options for expansion or restructuring.  However, the company wants to know what impact these changes will have on its base year emissions, as it works toward achieving a corporate GHG reduction target.  Indicate whether each change in EnviroCorp’s operations would necessitate a recalculation of its base year emissions.  Mention any assumptions on which your answer depends.

| Changes to EnviroCorp’s Operations | Is a base year recalculation needed? Why or why not? |
| --- | --- |
| EnviroCorp merges with neighboring SecondGen Renewable Energy Company |  |
| Heat is no longer produced on-site; it is outsourced to a third party. |  |
| Seven facilities are sold to MonoPower, a large power conglomerate |  |
| Continuous Emissions Monitoring Systems (CEMS) are installed in all of EnviroCorp’s facilities and the company undergoes rigorous research and testing to determine site-specific emissions factors. |  |
| EnviroCorp changes its production mix of electricity and heat from 70% electricity-30% heat to 65% electricity-35% heat. |  |
| The company acquires a brand new production facility. |  |

2. A company has the following information available relating to its Scope 1, 2 and 3 emissions:

| 2005 | 2006 | 2007 | 2008 |
| --- | --- | --- | --- |
| Scope 1 |  | Scope 1 | 4000 | Scope 1 | 4500 | Scope 1 | 5000 |
| Scope 2 | 7000 | Scope 2 | 8000 | Scope 2 | 8000 | Scope 2 | 9000 |
| Scope 3 |  | Scope 3 |  | Scope 3 |  | Scope 3 | 9000 |

Which year should it select as its base year and why?

3.  Answer the questions below based on the following scenario:

- G is a medium-sized bank.

- H is a small bank.

- In year 3 G acquired H.

- Base year, year 2 and year 3 emissions are given for both banks below.

| Bank G |
| --- |
| Base year | Year 2 | Year 3 (G acquires H) |
| 10,000 | 10,000 | 13,000 |

| Bank H |
| --- |
| Base year | Year 2 | Year 3 (acquired by G) |
| 3000 | 3000 | n/a |

Should G’s base year emissions be recalculated?

If so, what would G’s recalculated base year emissions be?

4.  Answer the questions below based on the following scenario:

- J is a car factory.

- K is a tire factory.

- In the base year and year 2, J manufactured its own tires.

- In year 3, J outsourced production of its cars’ tires to company K.

- Scope 1 emissions from the base year, year 2 and year 3 are given for both manufacturing companies below.

| Car factory J SCOPE 1 Emissions |
| --- |
| Base year (J produces tires in-house) | Year 2 (J produces tires in-house) | Year 3 (J outsources tire production to K) |
| Body parts | 20.000 | Body parts | 20.000 | Body Parts | 20.000 |
| Tires | 4.000 | Tires | 5.000 | Tires | 0.0 |

| Tire factory K SCOPE 1 Emissions |
| --- |
| Base year | Year 2 | Year 3 (J outsources tire production to K) |
| Tires (manufactured for J) | 0.0 | Tires (manufactured for J) | 0.0 | Tires (manufactured for J) | 5.000 |

Should J’s base year emissions be recalculated?

If so, what would J’s recalculated base year emissions be?

5.  Answer the questions below based on the following scenario:

- M is a paper company.

- There is increased demand for paper, so M opens up a new paper plant in year 3.

- Base year, year 2 and year 3 emissions are given for M below.

| Paper company M |
| --- |
| Base year | Year 2 | Year 3 (M opens a new paper plant) |
| 4.000 | 5.000 | 13.000 |

Should M’s base year emissions be recalculated?

If so, what would M’s recalculated base year emissions be?

6. Answer the question below based on the following scenario:

- Company P originally calculated the following emissions for its base year, year 2 and year 3:

| Company P |
| --- |
| Base year | Year 2 | Year 3 |
| 100.000 | 105.000 | 103.000 |

- A review of the company’s emissions data revealed calculation errors.

- Company P corrected for these errors and reported the following correct emissions:

| Company P (corrected emissions) |
| --- |
| Base year | Year 2 | Year 3 |
| 101.000 | 103.000 | 102.000 |

Assuming Company P has set a 5% significance threshold, should its base year emissions be recalculated?

7. Answer the question below based on the following scenario:

- Company S originally calculated the following emissions for its base year, year 2 and year 3:

| Company S |
| --- |
| Base year | Year 2 | Year 3 |
| 250.000 | 275.000 | 300.000 |

- A review of the company’s emissions data revealed that when calculating its emissions, Company S had mistakenly used an emission factor for Clean Development Mechanism projects instead of the emission factor for corporate inventories.

- Company P corrected for these errors and reported the following correct emissions:

| Company S (corrected emissions) |
| --- |
| Base year | Year 2 | Year 3 |
| 75.000 | 80.000 | 83.000 |

Assuming Company S has set a 5% significance threshold, should its base year emissions be recalculated?