1.  Calculating Direct Emissions from Stationary Combustion

Annual Consumption of Fuels

F&M is a manufacturing facility with two 10 MW generating units, one burning natural gas and one coal-fired unit.  F&M also has a commercial office building on-site that is heated with diesel.  Last year, the company consumed 20,000,000 standard cubic meter (m3) of natural gas and 40,000 metric tons of coal in the generating units.  F&M also began the year with 41900 litres of diesel in storage and ended the year with 6000 litres in storage; it combusted the rest of the diesel.

Calculate the company’s total emissions of carbon dioxide (CO2) from stationary combustion.

Assume the following emission factors:

Natural gas: 		1.9141 kg CO2/ m3

Coal: 		2274.69 kg CO2/ metric ton

Diesel: 		2.6533 kg CO2/ litre

Answer:

Step 1: Calculate annual diesel use by taking into account purchase, sale and inventory stock.

| Step 1 | Stationary Combustion Example: Accounting for Changes in Fuel (Diesel) Stocks |
| --- | --- |
| Annual Diesel Consumption = Diesel Stock at Start of Year - Diesel Stock at End of Year (litres) (litres) (litres) = 41900 litres - 6000 litres = 35900 litres |

Step 2: Calculate CO2 emissions for each fuel using respective emission factor.  Add to obtain total CO2 emissions for F&M.

| Step 2 | Stationary Combustion Example: Calculating CO2 Emissions Using Emission Factor |
| --- | --- |
| Fuel A CO2 Emissions = Fuel Consumed × Emission Factor ÷ 1,000 (metric tons) (metric unit) (kg CO2/metric unit) (kg/metric ton) |
| Natural Gas CO2 Emissions = 20,000,000 × 1.9141 ÷ 1000 = 38,282 metric tons (metric tons) (cubic meter) (kg CO2/cubic meter) (kg/metric ton) |
| Coal CO2 Emissions = 40,000 × 2274.69 ÷ 1000 = 90987.6 metric tons (metric tons) (metric tons) (kg CO2/metric ton) (kg/metric ton) |
| Diesel CO2 Emissions = 35900 × 2.6533 ÷ 1,000 = 95.25 metric tons (metric tons) (litre) (kg CO2/litre) (kg/metric ton) |
| Total CO2 Emissions = 38,282 + 90987.6 + 95.25 = 129,364.85 metric tons (metric tons) (metric tons) (metric tons) (metric tons) |

2. Calculating Direct Emissions from Mobile Combustion

GOFAST Vehicle Rental is an independent vehicle renting company with a fleet of 200 passenger cars (model year 2000), 25 light duty trucks (model year 2002), and two heavy duty diesel powered trucks (model year 1998).  GOFAST typically purchases its fuel in bulk.  Last year, the company purchased 900,000 litres of motor gasoline and 20,000 litres of diesel fuel.  The company began the year with 75,000 litres of motor gasoline in stock and ended with 40,000 litres of motor gasoline in stock.  The company also began the year with 2000 litres of diesel fuel in stock and ended with 4,000 litres of diesel fuel in stock.  GOFAST also keeps odometer readings for each vehicle and determines total mileage by vehicle type as follows: 9,700,000 kilometer for passenger cars; 890,000 kilometer for light trucks; and 130,000 kilometer for heavy duty trucks.

Calculate GOFAST’s emissions of carbon dioxide (CO2), methane (CH4) and nitrous oxide (N2O) from mobile combustion.

Assume the following emission factors:

Gasoline: 					    	2.30 kg CO2/ litre

Diesel: 					    	2.6533 kg CO2/ litre

Passenger car (gasoline, model year – 2000):  	0.022494 g N2O/ km;   0.027216 g CH4/ km

Light Duty trucks (gasoline, model year – 2002): 	0.023488 g N2O/ km;   0.030509 g CH4/ km

Heavy Duty trucks (diesel, model year – 1998): 	0.002983 g N2O/ km;   0.003169 g CH4/ km

Answer:

Step 1: Calculate annual diesel and gasoline use by accounting for purchase and inventory stock at the beginning and end of year.

Total Annual Fuel C

| Step 1 | Accounting for Changes in Fuel Stocks From Bulk Purchases |
| --- | --- |
| Annual Consumption = Total Annual Fuel Purchases + Amount Stored at Beginning of Year – Amount Stored at End of Year |
| Total Gasoline Consumption = 900,000 + 75,000 – 40,000 = 935,000 (litres) (litres) (litres) (litres) (litres) |
| Total Diesel Consumption = 20,000 + 2000 – 4,000 = 18,000 (litres) (litres) (litres) (litres) (litres) |

Step 2: Calculate CO2 emissions for each fuel using respective emission factor.  Sum to obtain total CO2 emissions for GOFAST.

| Step 2 | Calculating CO2 Emissions From Mobile Combustion |
| --- | --- |
| CO2 Emissions = Fuel Use × Emission Factor ÷ 1,000 (metric tons) (metric unit) (kg CO2 /metric unit) (kg/metric tons) |
| Gasoline CO2 Emissions = 935,000 × 2.30 ÷ 1,000 = 2,150.5 (metric tons) (litre) (kg CO2 /litre) (kg/metric tons) (metric tons CO2) |
| Diesel CO2 Emissions = 18,000 × 2.6533 ÷ 1,000 = 47.76 (metric tons) (litre) (kg CO2 /litre) (kg/metric tons) (metric tons CO2) |
| Total CO2 Emissions = 2,150.5 + 47.76 = 2,198.26 (metric tons) (metric tons) (metric tons) (metric tons CO2) |

Step 3:  Identify the vehicle type, fuel, model year, number of vehicles, mileage and corresponding emission factors for N2O and CH4.  (This information is given.)

| Step 3 | Identify vehicle type, fuel, model, number of vehicles, mileage and emission factor |
| --- | --- |
| Vehicle Type | Fuel | Model Year | No. of Vehicles | Mileage (km) | g CH4 / km | g N2O / km |
| Passenger Cars | Motor Gasoline | 2000 | 200 | 9,700,000 | 0.0272 | 0.0225 |
| Light Duty Trucks | Motor Gasoline | 2002 | 25 | 890,000 | 0.0305 | 0.0235 |
| Heavy Duty Trucks | Diesel | 1998 | 2 | 130,000 | 0.0032 | 0.0030 |

Step 4:  Calculate CH4 and N2O emissions associated with each vehicle type, and sum to obtain total CH4 and N2O emissions.

| Step 4 (i) | Calculating N2O Emissions From Mobile Combustion |
| --- | --- |
| Passenger Cars N2O Emissions = 9,700,000 × 0.0225 ÷ 1,000,000 = 0.2183 (metric tons) (km) (g N2O/km) (g / metric ton) (metric ton N2O) |
| Light Duty Trucks N2O Emissions = 890,000 × 0.0235 ÷ 1,000,000 = 0.0209 (metric tons) (km) (g N2O/km) (g / metric ton) (metric ton N2O) |
| Heavy Duty Trucks N2O Emissions = 130,000 × 0.0030 ÷ 1,000,000 = 0.0004 (metric tons) (km) (g N2O/km) (g / metric ton) (metric ton N2O) |
| Total N2O Emissions = 0.2183 + 0.0209 + 0.0004 = 0.2396 (metric tons) (metric tons) (metric tons) (metric tons) (metric tons N2O) |

| Step 4 (ii) | Calculating CH4 Emissions From Mobile Combustion |
| --- | --- |
| Passenger Cars CH4 Emissions = 9,700,000 × 0.0272 ÷ 1,000,000 = 0.2638 (metric tons) (km) (g CH4/km) (g / metric ton) (metric ton CH4) |
| Light Duty Trucks CH4 Emissions = 890,000 × 0.0305 ÷ 1,000,000 = 0.0271 (metric tons) (km) (g CH4/km) (g / metric ton) (metric ton CH4) |
| Heavy Duty Trucks CH4 Emissions = 130,000 × 0.0032 ÷ 1,000,000 = 0.0004 (metric tons) (km) (g CH4/km) (g / metric ton) (metric ton CH4) |
| Total CH4 Emissions = 0.2638 + 0.0271 + 0.0004 = 0.2913 (metric tons) (metric tons) (metric tons) (metric tons) (metric tons CH4) |

Step 5:  Convert CH4 and N2O emissions to units of CO2-equivalent and determine total emissions from mobile combustion.

| Step 5 | Converting to CO2-equivalents and determining total emissions |
| --- | --- |
| CO2 Emissions = 2,198.26 × 1 = 2,198.26 (metric tons CO2-e) (metric tons CO2) (GWP) (metric tons CO2-e) |
| CH4 Emissions = 0.2913 × 21 = 6.117 (metric tons CO2-e) (metric tons CH4) (GWP) (metric tons CO2-e) |
| N2O Emissions = 0.2396 × 310 = 74.276 (metric tons CO2-e) (metric tons N2O) (GWP) (metric tons CO2-e) |
| Total Emissions = CO2 + CH4 + N2O = 2,278.653 (metric tons CO2-e) (metric tons CO2-e) (metric tons CO2-e) |

3. Calculating Indirect Emissions from Electricity Use (location-based method)

Cost-lo is a discount retail clothing chain with one outlet in Sao Paulo, Brazil. Cost-lo records its annual electricity purchases in megawatt-hours (MWh) and for the last year, its electricity consumption was 1600 MWh.

Calculate location-based CO2 emissions from electricity use for Cost-lo.

Assume the following location-based, grid-average emission factor (expressed in CO2, as N2O and CH4 emission rates are not available): 0.5727 t CO2/ MWh.

Answer:

Step 1: Calculate total emissions from electricity use using annual consumption and location-based emission factor.

| Step 1 | Calculating Indirect Emissions from Electricity Use |
| --- | --- |
| CO2 Emissions = 1,600 × 0.5727 = 916.32 (MWh) (t CO2/ MWh) (metric tons CO2) |

4. Calculating Indirect Emissions from Electricity Use (market-based method)

Cost-lo entered into a contract to purchase 50% of its energy from hydropower to cover its electricity consumption. The other 50% of the supply comes from their utility, who supplies Cost-lo with a supplier-specific emission factor. Both of these contractual instruments meet the Scope 2 Quality Criteria for the market-based method. Assume total electricity consumption of 800 MWh.

Calculate the market-based CO2 emissions from electricity use for Cost-lo.

Assume the following supplier-specific emission factor (expressed in CO2, as N2O and CH4 emission rates are not available):  0.70 t CO2 / MWh

Answer:

Step 1: Apply the contract-specific emission rate of 0 t CO2 /MWh  to half the overall consumption (400 MWh), and the supplier-specific emission rate of .7 t CO2 /MWh  to the other half of the power

| Step 1 | Calculating Indirect Emissions from Electricity Use |
| --- | --- |
| CO2 Emissions = 400 × 0 + 400 x 0.70 = 280 (MWh) (t CO2/ MWh) (MWh) (t CO2/ MWh) (metric tons CO2) |

CALCULATING EMISSIONS USING GHG PROTOCOL TOOLS

Calculation tools publicly available and the GHG Protocol website can make calculating emissions easier.  The tools have been reviewed by industry experts and are regularly updated.

http://www.ghgprotocol.org/calculation-tools

5. Using GHG Protocol tools to calculate emissions from employee business travel

Chicago Accounting is based in the United States.  Chicago Accounting’s staff makes regular business trips to client offices.  To complete all business trips in the reporting year, company-owned cars (all of which were purchased new in 2007) consumed a total of 14,755 gallons of gasoline, and employees traveled a total of 330,500 miles on domestic commercial airline flights.

Calculate Chicago Accounting’s emissions from business trips in the reporting year.

(Hint: Use the GHG Protocol’s GHG emissions from transport or mobile sources tool)

Answer:

Step 1: Open the GHG emissions from transport or mobile sources tool.

Step 2: Click on “Enter Activity Data” (or open the Activity Data worksheet by clicking on the “Activity Data” tab at the bottom of your screen).

Step 3: Fill in the following information in the required fields:

| Status | Source Description | Region | Mode of Transport | Scope | Type of Activity Data | Activity Data |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Vehicle Type | Distance Travelled | Gross Weight | # of Passenger | Unit of Distance | Fuel Used | Fuel Amount | Unit of Fuel Amount |
|  | Client visits (company-owned cars) | US | Road | Scope 1 | Fuel Use | Passenger Car - Gasoline - Year 2005-present |  |  |  |  | Gasoline/ Petrol | 14755 | US Gallon |
|  | Client visits (domestic flights) | US | Aircraft | Scope 3 | Passenger Distance (e.g. Public Transport) | Air - Domestic | 330500 |  | 1 | Passenger Mile |  |  |  |

Step 4: Open the Summary worksheet by clicking on the “Summary” tab at the bottom of your screen.  Find total Scope 1 and Scope 3 emissions.

Chicago Accounting’s emissions from business trips in the reporting year:

Scope 1 (from company-owned cars):			130.823 t CO2e

Scope 3 (from non-company owned planes): 	91.203 t CO2e

(Note: CH4 and N2O emissions from air travel are not accounted for in the GHG Protocol transport tool.   Emission factors are unavailable for CH4 and N2O from air travel as they represent an extremely small proportion of the climate impact of aviation.)

6. Using GHG Protocol tools to calculate emissions from purchased electricity (location-based method)

Office Associates, Inc., based in New York, shares a 200,000 square foot building with Business Analysts, Inc.  Both firms own 100,000 square-feet of the building and split the electricity bill fifty-fifty.  To calculate its emissions, Office Associates gathered data from the building’s electricity bill.  The building’s total electricity usage for the reporting year, 2005, was 1,900,250 kWh.

Calculate Office Associates’ emissions from purchased electricity in 2005.

(Hint: Use the GHG Protocol’s GHG emissions from Purchased Electricity, Heat or Steam tool.)

Answer:

Step 1: Open the GHG emissions from Purchased Electricity, Heat or Steam tool.

Step 2: Open the Spreadsheet worksheet by clicking on the “Spreadsheet” tab at the bottom of your screen.

Step 3: Fill in the following information in the required fields:

| Facility information | Consumption data |
| --- | --- |
| Facility description | % of electricity used by the facility | Country | Region (if available) | Year | Fuel mix | Amount | Units |
| Office Building | 50 | United States | NPCC NYC/Westchester | 2005 |  | 1900250 | kWh |

Step 4: Find total emissions in the “CO2e (tonnes)” column

Office Associate’s emissions from purchased electricity in the reporting year:

Scope 2:							352.49 t CO2e