You were contracted by Ice Cold Beverages (an imaginary company) to complete its first GHG emissions inventory, for calendar year 2009.  Information about the company’s structure and data about its activities are provided below.  Use the template provided on the last page of this exercise to complete Ice Cold’s GHG inventory.

Ice Cold’s management has asked that you use the operational control consolidation approach in determining organizational boundaries.  Also, because a fixed amount of time has been allotted to completion of this exercise, please only account for Scopes 1 and 2.

Desciption:  Ice Cold Beverages

Ice Cold is a small beverage company that started operations in 1999. Today, Ice Cold has a 10% beverage market share in its region, and it consists of a central office, two beverage production plants, a distribution center and a delivery vehicle fleet.

Since management has decided to use the operational control consolidation approach, consult Ice Cold’s structure to determine whether it has control of the operations of each of the facilities. According to the operational control consolidation approach, a reporting company will report 100% of the emissions of facilities it controls and 0% of the emissions of facilities is does not control.

See organizational boundary answers in black boxes below

Structure of Ice Cold Beverages

Data for Ice Cold’s facilities

Central Office

Ice Cold’s central office is located in New York City.  The central office is in a commercial building and occupies 1,000 m2 of the second floor, which is a total of 4,000 m2.  The electricity consumed monthly by the entire second floor is shown in the table below:

Table 1: Monthly electricity consumption of second floor

| Month | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sept | Oct | Nov | Dec |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| kWh | 1610 | 1755 | 1770 | 1565 | 1735 | 1645 | 1655 | 1605 | 1640 | 1595 | 1655 | 1510 |

In addition, Ice Cold’s central office purchases renewable energy certificates (RECs) through a green label offered by the local electric utility. These purchases are made by the building owner to cover 100% of all electricity consumed in the building. These RECs meet the Scope 2 Quality Criteria.

To calculate the market-based method total: Determine Ice Cold’s total electricity consumption for the year, by multiplying the total floor’s use (19,740 kWh) by .25 to determine the amount attributable to Ice Cold. Multiply consumption by the emission factor conveyed by the contractual instrument – here, RECs that cover 100% of consumption. (0 kg CO2/kWh x 4,935 kWh = 0 kg CO2. Convert to tons = 0 kg CO2. * For reporting, need to indicate that a residual mix is not available for the U.S. currently (see Scope 2 Quality Criteria). To calculate the location-based method total: Open the GHG Protocol calculation tool “GHG emissions from Purchased Electricity, Heat, or Steam.” Click on the Spreadsheet tab at the bottom. Add up the total kWh of electricity used for the year (19,740 kWh). Fill in the following information in the tool: Facility information Consumption data Facility description % of electricity used by the facility Country Region (if available) Year Fuel mix Amount Units Central Office 25 United States NPCC NYC/ Westchester 2009 19,740 kWh Find the total location-based CO2e: 1.37 tCO2e

Ice Cold’s central office is also equipped with central air conditioning.  The air conditioning equipment uses the refrigerant R-410A, of which there was 30 kg in storage at the beginning of 2009 (the reporting year), and 10 kg in storage at the end of the year.  Over the reporting period, no refrigerant or air-conditioning equipment was purchased and no refrigerant was transferred offsite (e.g., sold to other companies or destroyed).

Open the GHG Protocol calculation tool “GHG emissions from refrigeration and air-conditioning.” Click on the “WS 1b – Sales Approach (User)” tab at the bottom of the spreadsheet. Fill in the following information in the tool for R-410A in the “Refrigerant Used” column: Step 1 Step 2 Step 3 Step 4 Step 5 Equipment and Refrigerant Type Decrease in Inventory (kilograms) A B C D E Type of Air Conditioning and Refrigeration Equipment Refrigerant Used Refrigerant inventory (in storage, not equipment) at the beginning of the year Refrigerant inventory (in storage, not equipment) at the end of the year Decrease in Refrigerant Inventory E = C - D R-410A 30.00 10.00 20.00 Find the total CO2e: 34.50 (Scope 1)

The sales team based in Ice Cold’s central office uses company-owned vehicles for sales trips.  The company-owned vehicles were purchased in 2007 and are only used for business travel.  Ice Cold recorded each car’s odometer at the beginning and end of the year to find that during the entire year, all company owned cars traveled a total of 450,000 miles. The vehicles are gasoline (petrol)-powered passenger cars.

| Open the GHG Protocol calculation tool “GHG emissions from transport or mobile sources.” Click on “Enter Activity Data.” Fill in the following information in the tool: Status Source Description Region Mode of Transport Scope Type of Activity Data Activity Data Vehicle Type Distance Travelled Gross Weight # of Passenger Unit of Distance Fuel Used Fuel Amount Unit of Fuel Amount  Central Office car fleet US Road Scope 1 Vehicle Distance (e.g. Road Transport) | Passenger Car - Gasoline - Year 2005-present 450000 Mile Find the total CO2e in the Summary worksheet: 177.33 (Scope 1) |
| --- | --- |
| Production Plant A |

Ice Cold’s Production Plant A, located in Mexico, gets all of its electricity from a local electric utility who discloses a CO2 emission factor of 0.252 kg CO2/kWh (emission factors for CH4 and N2O are unavailable).  That supplier-specific emission rate meets the Scope 2 Quality Criteria.

Production Plant A’s complete monthly electricity usage is shown in the table below. Because it has access to product or supplier-specific information, Ice Cold will report two scope 2 numbers: one location-based, and one-market-based.

Table 2: Total monthly electricity consumption for Production Plant A

| Month | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sept | Oct | Nov | Dec |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| kWh | 26770 | 26110 | 25040 | 22565 | 23355 | 22325 | 20615 | 21660 | 25935 | 27740 | 29395 | 29935 |

To calculate the market-based method total: Determine Ice Cold’s total electricity consumption for the year (301,445 kWh) Multiply consumption by the emission factor conveyed by the supplier– here, (.252 kg CO2/kWh x 301,445 kWh) = ANSWER: 75,964.14 kg CO2. Convert to metric tons = 75.964 t CO2 * For reporting, need to indicate that a residual mix is not available for Mexico currently (see Scope 2 Quality Criteria). To calculate the location-based method total: Open the GHG Protocol calculation tool “GHG emissions from Purchased Electricity, Heat, or Steam.” Click on the Spreadsheet tab at the bottom. Add up the total kWh of electricity used for the year (301,445 kWh). Select “Mexico” Facility information Consumption data Emission factor (kg GHG/ KWh) Facility description % of electricity used by the facility Country Region (if available) Year Fuel mix Amount Units CO2 CH4 N2O Production Plant A 100 Mexico 2009 All 301445 kWh *not visible Find the total tons CO2e (location-based): 137.15

The production processes at Production Plant A are powered by energy generated on-site from combustion of both diesel oil and natural gas.  In 2009, Production Plant A combusted 7,500 litres of diesel oil and 1,000 m3 of natural gas.

Open the GHG Protocol calculation tool “GHG emissions from stationary combustion.” Click on the Spreadsheet tab at the bottom. Fill in the following information in the tool: Source ID Sector Fuel type (e.g., solid fossil) Fuel Amount of fuel Units (e.g., kg or kWh) Heating value basis Production Plant A Manufacturing Liquid fossil Gas/ Diesel oil 7500 litres (l) Not applicable Production Plant A Manufacturing Gaseous fossil Natural gas 1000 metre3 Not applicable Find the total CO2e: 22.03 (Scope 1)

Factory B

Ice Cold’s Factory B, also located in Mexico, formed a power purchase agreement with a wind  farm development. The contract specifies the delivery of 0 t CO2/ kWh, and meets the Scope 2 Quality Criteria (emission factors for CH4 and N2O are unavailable).  Factory B’s complete monthly electricity usage is shown in the table below.

Table 3: Total monthly electricity consumption for Factory B

| Month | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sept | Oct | Nov | Dec |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| kWh | 19274 | 18799 | 18029 | 16247 | 16816 | 16074 | 14843 | 15595 | 18673 | 19973 | 21664 | 21553 |

A boiler in Factory B combusts liquified petroleum gas (LPG) to power production processes.  Ice Cold’s financial records indicate that 84,600 kg of LPG were purchased and used throughout the year.

Factory B also utilizes a refrigerating unit, which uses HFC-134a, for cooling purposes during the production process.  At the beginning of the year, Ice Cold had 1000 kg of HFC-134a in storage, and by the end of the year, it only had 200 kg of HFC-134a remaining in storage.

“Big Beverages” controls all of Factory B’s operations, so Factory B is not under the operational control of Ice Cold. Therefore, none of Factory B’s emissions should be accounted for in Ice Cold’s GHG inventory under Scope 1 or 2. Emissions from Factory B could optionally be reported under Scope 3.

Ice Cold Vehicle Fleet

Ice Cold has its own fleet of trucks to transport beverages between Production Plant A, Factory B and its distribution center.  Over the course of the entire year, Ice Cold purchased and consumed 968,500 gallons of diesel for use in its fleet of heavy duty (rigid) trucks.  (The truck fleet is based in the United States.)

Open the GHG Protocol calculation tool “GHG emissions from transport or mobile sources.” Click on “Enter Activity Data.” Fill in the following information in the tool: Status Source Description Region Mode of Transport Scope Type of Activity Data Activity Data Vehicle Type Distance Travelled Gross Weight # of Passenger Unit of Distance Fuel Used Fuel Amount Unit of Fuel Amount Ice Cold Vehicle Fleet US Road Scope 1 Fuel Use Heavy Duty Vehicle - Rigid - Diesel - Year 1960-present On-Road Diesel Fuel 968500 US Gallon Find the total CO2e in the Summary worksheet: 9842.22 (Scope 1)

Distribution Center

The Ice Cold Distribution Center is located in Texas and gets all of its electricity from the ERCOT regional grid.  It also purchases renewable energy certificates (RECs) to match 50% of its consumption. These RECs meet the Scope 2 Quality Criteria. There is no residual mix available in the U.S. currently for the market-based method calculation.

Because it has access to product or supplier-specific information, Ice Cold will report two scope 2 numbers: one location-based, and one-market-based. Ice Cold used its monthly energy bills to determine its entire monthly electricity consumption, shown in the table below:

Table 4: Total monthly electricity consumption for the Ice Cold Distribution Center

| Month | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sept | Oct | Nov | Dec |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| kWh | 3855 | 3760 | 3606 | 3249 | 3363 | 3215 | 2969 | 3119 | 3735 | 3995 | 4233 | 4311 |

To calculate the market-based method total: Determine Ice Cold’s total electricity consumption for the year (43,410 kWh) Determine 50% of the consumption, which will use the REC emission factor (21,705). Multiply this consumption by the emission factor conveyed by the REC purchase– here, (0 kg CO2/kWh x 21,705 kWh)= 0 kg CO2, converted to tons = 0 t CO2 In absence of other supplier-specific information or a residual mix, use location-based method data to determine emissions from rest of consumption. For using location-based data for remainder, use GHGP tool. Input 21,705 into calculation tool, multiply by US—ERCOT factor (see below for Market-based Method (MBM)) * For reporting, need to indicate that a residual mix is not available for US currently (see Scope 2 Quality Criteria). Facility description % of electricity used by the facility Country Region (if available) Year Fuel mix Amount Units M B M Distribution Center 50 United State ERCOT 2009 21, 705 kWh Total emissions from energy matched with REC purchases = 0 t CO2 Total emissions from remaining energy (21,705 kWh) = 11.67 t CO2 TOTAL in market-based method = 0 + 11.67 = 11.67 t CO2 To calculate the location-based method total: Open the GHG Protocol calculation tool “GHG emissions from Purchased Electricity, Heat, or Steam.” Click on the Spreadsheet tab at the bottom. Add up the total kWh of electricity used for the year (43,410 kWh). Fill in the following information in the tool (see Location-based Method (LBM) row below); Facility information Consumption data Facility description % of electricity used by the facility Country Region (if available) Year Fuel mix Amount Units L B M Distribution Center 100 United States ERCOT 2009 43410 kWh Find the total location-based CO2e: 23.35 t CO2e

Quicky’s Delivery Fleet

Quicky’s Delivery Fleet is an independently owned and operated company to which Ice Cold has outsourced the transportation of beverages from the Ice Cold Distribution Center to all retail outlets.  Each year Quicky’s provides Ice Cold with a record of total miles traveled for the delivery of Ice Cold beverages.  In 2009, Quicky’s vehicles traveled 760,800,000 miles within the United States via its fleet of heavy duty (rigid) diesel trucks while providing delivery services to Ice Cold.

Quicky’s Delivery Fleet is 100% operated by Quicky’s, so Ice Cold does not have operational control over these vehicles. Therefore, none of the emissions from Quicky’s Delivery Fleet vehicles should be accounted for in Ice Cold’s GHG inventory as Scope 1 or 2, although they could optionally be reported as Scope 3.

Total emissions:

| Facility | Emissions source | Scope 1 | Scope 2 (market-based) | Scope 2 (location-based) |
| --- | --- | --- | --- | --- |
| Central Office | electricity |  | 0 | 1.37 |
|  | air conditioning | 34.500 |  |  |
|  | cars - sales trips | 177.33 |  |  |
| Production Plant A | electricity |  | 75.96 | 137.15 |
|  | on-site combustion | 22.03 |  |  |
| Ice Cold Vehicle Fleet | truck fleet | 9,842.33 |  |  |
| Distribution Center | electricity |  | 11.67 | 23.35 |
| TOTAL |  | 10,076.19 | 87.63 | 161.87 |

GHG Inventory:  Ice Cold Beverages

Organizational Boundaries

| Consolidation Approach Chosen | Operational Control |
| --- | --- |

| Facilities included in GHG inventory | Central Office |
| --- | --- |
|  | Production Plant A |
|  | Ice Cold Vehicle Fleet |
|  | Distribution Center |

Operational Boundaries

| Operational Boundaries (Scopes included) | Scopes 1 and 2 |
| --- | --- |
| Reporting Period | 1 January 2009 – 31 December 2009 |

Tracking Emissions Over Time

| Base year and emissions profile over time | Base year: 2009 This is Ice Cold’s first inventory, so 2009 will be its base year. Since this is the first GHG inventory Ice Cold has completed, its emissions profile over time cannot be provided. |
| --- | --- |

Emissions Calculations

| Total Scope 1 and 2 emissions (using market-based method) | 10,163.82 |
| --- | --- |
| Total Scope 1 and 2 emissions (using location-based method) | 10,238.06 |
| Total Scope 1 emissions | 10,076.19 |
| Total Scope 2 emissions (market-based) | 87.63 |
| Total Scope 2 emissions (location-based) | 161.87 |